## Slide 1: ECHOCARDIOGRAPHY-BASICS
Dr.Muhammad Ameen C
Senior Resident-Cardiology
GMCH Kozhikode

## Slide 2: Echocardiography
Technique of using ultrasound to examine the heart and great vessels

## Slide 3
Father of ultrasound

## Slide 6: Principle of ultrasound
Sound
  Mechanical disturbance transmitted through a medium
Properties
  Frequency:number of times per sec,sound undergoes a cycle of rise and fall(Hz). Appreciated as pitch
  Wavelength:distance travelled in one cycle
  Velocity : depends on medium
  Intensity/Amplitude:loudness(dB)

## Slide 11: Characteristics of US
Can be directed as a beam and focused
Obeys the rules of reflection and refraction
Targets of relatively small size reflect US and can be detected and characterized

## Slide 12: Disadvantages
Ultrasound is poorly transmitted through a gaseous medium
Attenuation occurs rapidly, especially at higher frequency

## Slide 13: Mechanics
Relies on piezoelectric effect
Property to transform electrical current into ultrasound waves

## Slide 14
Reflected signal gives information about the depth and nature of tissue studied
Most reflection occurs at tissue interfaces
Reflectivity
  High:white (bone)
  Low:grey (muscle)
  Nil:black (air)

## Slide 15: Pulse repetition period

## Slide 16
Location of image depends on time lag between transmission and reflection of US

## Slide 17: Equipment -Echograph
Transducers
Monitor
Processing unit

## Slide 18: Transducer
Contains piezoelectric crystals
Generate and receive sound waves

## Slide 19
Piezoelectric ceramics : ferroelectrics, barium titanate, and lead zirconate titanate
Piezoelectric elements are interconnected electronically
The frequency of the transducer is determined by the thickness of these elements.
Each element is coupled to electrodes, which transmit current to the crystals, and then record the voltage generated by the returning signals.
Piezoelectricity

## Slide 20: Cardiac transducer
Electric force<>deformation<>US waves
Phased array
1-5 MHz
Orientation : notch/groove/ridge
Screen orientation : marker on upper right of image
Most fragile part of system. Can be easily damaged

## Slide 22: Transducer
↑frequency -↓wavelength-↓penetration-↑resolution
↓frequency-↑wavelength-↑penetration-↓resolution

## Slide 25: Intracardiac probe

## Slide 26: Frequency
Neonates : 7.0-7.5 MHz
Children : 3.5-5.0 MHz
Adults : 2.0-2.5 MHz

## Slide 28: Transducer technology
Linear array
Phased array

## Slide 32: Wave motion
An ultrasound beam as it leaves the transducer is parallel and cylindrically shaped beam. Eventually, however, the beam diverges and becomes cone shaped .
The proximal or cylindrical portion of the beam is referred to as the near field or Fresnel zone.
When it begins to diverge, it is called the far field or Fraunhofer zone.

## Slide 35: Transducer adjustments
Alignment
Rotation
Tilt

## Slide 36: Behaviour of US in tissue
Reflection: specular echoes at interfaces
Refraction: change in direction due to change in speed
Scattering: when encounter small structures
Attenuation:loss of US as it propagates through a medium

## Slide 39: Attenuation

## Slide 40: Modalities
2D
3D
4D
M mode

## Slide 42: A(amplitude) mode
Oldest type
Amplitude is plotted against distance
Not in clinical use

## Slide 43: B mode
Brightness mode
Amplitude is recorded as brightness

## Slide 44: M(Motion) Mode
One scan line
Higher frame rate
High sensitivity for movement
High temporal resolution
To assess
  Cavity size and wall thickness
  Excursion of walls and cusps
  Timing of cardiac events

## Slide 45: 2D Echo
Electric signal produces a dot on display
Density and position of dot is determined by nature and depth of tissue
90-120 scan lines
90 ̊ arc
To evaluate
  Anatomy of heart
  Intracardiac mass

## Slide 47: 3D
Recreated from multiple 2D planes
Depth as an additional dimension
Done by imaging along a pyramidal US beam
True live or near real-time images
Real time 3D is known as 4D
Post processing, slicing and cropping possible
Best for evaluation of valvular disease, chamber volume and function
Limitation : stitching artefact

## Slide 51: Harmonic imaging
Tissues resonate at multiples of transmitted frequency (harmonic frequencies)
Transducer receives frequencies at multiples of the emitted frequency
Improves signal-to-noise ratio
Better delineation of endocardial border
Disadvantage:valve leaflets may appear artificially thick

## Slide 53: Image resolution
Ability to distinguish two objects that are close together
Teomporal : with respect to time
Spatial
  Axial :parallel to US beam (objects above and below)
  Lateral : perpendicular to US beam (objects side by side)

## Slide 55: Depth
Set 1-2cm beyond cardiac boundary

## Slide 56: Gain
Controls overall amplification of the echo signals
Intracardiac blood should be as dark as possible without losing definition of walls

## Slide 58: Time gain compensation
Little difference in densities of blood, musle and fat
Echoes from interfaces will be small
TGC increases amplification during the time echoes from a particular pulse returns
The last to arrive are amplified much more than the first

## Slide 60: Depth gain compensation
Near field objects appear brighter
Depth specific amplification of echo signals

## Slide 61: Focal position
Controls the depth at which US beam is focused
Around this region spatial resolution is optimal

## Slide 62: Frame rate
Number of still images displayed per unit time
Controls number of lines in single frame and number of frames per second
Higher the frame rate, better the temporal and worse the spatial resolution

## Slide 63: Artefacts
Flase, missing, mislocated or distorted structures
Caused by
  Interaction of US waves with tissues
  Physical properties of US beam
  Image reconstruction algorithms

## Slide 64: Side lobe artefact
A portion of energy concentrate off to the side of the central beam and propagate radially – edge effect
Seen in strongly reflecting targets
Most common: AV groove and fibrous skeleton

## Slide 66: Reverberation artefact
Produced by non-soft tissue structures
Reflected echoes bounce back and forth between the highly reflective object and the transducer
Seen in clacified/prosthetic valve
To avoid
  Use minimum power and adequate gel
  Rotate the paient or change the angle

## Slide 69: Shadowing
Seen in case of strong reflectors
Due to absence of echoes behind the target
Result of high attenuation of signals
Opposite of reverberation
Common in prosthetic valves

## Slide 71: Near-field clutter
Ringdown artefact
Arises from high-amplitude oscillations of the piezoelectric elements
Common in RV free wall and LV apex

## Slide 73: Mirror artefact
US beam takes an indirect return journey after hitting a reflective surface
True image above and mirror image below

## Slide 74: Tissue damage
Heating
  Due to too much acoustic energy
  Monitored by thermal index (TI)
  TI should be below 2
Cavitation
  Formation of small gas bubbles followed by collapse
  Monitored through mechanical index (MI)
  MI should remain below 1.9 (most scanners <1.1)

## Slide 75: Mechanical Index
Measure of mechanical pressure exerted on tissues by US waves
MI should be lowered during contrast echo to prevent early burst of bubbles

## Slide 76: Thermal index
Energy lost through attenuation is largely converted to heat
TI : ratio of actual beam power to that required to raise the temperature of a specific tissue by 1 ̊C
Important in TEE-minimised by automatic thermal cut-out mechanism

## Slide 77: Ergonomics and Set up
Comfortable height
Always use same hand
Lie down with abducted left arm
Avoid sunlight for optimal contrast
Explain the procedure
Privacy and need of chaperone

## Slide 78: Respiration
Acquire most views at held end-expiration
A2C and subcostal views at held end-inspiration

## Slide 79: Thank You