## Slide 1: Percutaneous treatment for Mitral Regurgitation
Presenter
Dr. Benny J. Panakkal
Senior Resident
Dept. of Cardiology
Govt. Medical College, Kozhikode.

## Slide 2: Transcatheter Mitral Valve Repair
TMVRe

## Slide 3: Overview
APPROACH | DEVICE
LEAFLET REPAIR | MITRACIP
 | MOBIUS
CORONARY SINUS ANNULOPLASTY | CARILLON
 | PTMA
 | MONARC
ATRIAL REMODELLING | PS3
 | PMVR
DIRECT ANNULOPLASTY | MITRALIGN
 | ACCUCINCH
 | QUANTUMCOR
 | HYBRID APPROACH
VENTRICULAR REMODELLING | iCOAPSYS
 | Mardil-BACE
CHORDAL IMPLANTATION | MITRAFLEX
 | NEOCHORD
 | BABIC

## Slide 4: Leaflet Repair

## Slide 5: MitraClip
Leaflet Repair
Notes: Mitraclip device with Evalve delivery system→ Alfieri repair
EVEREST I AND II trials: exclusion of patients with severe LV dys or annular dilatation→means only sev degenerative MR patients were studied.
EVEREST II randomized patients in 2:1 ration to mitraclip vs surgery

## Slide 6: Mobius
Leaflet Repair
Notes: Milano II trial→ very complex procedure, hence abandoned plans to pursue. Variable results.

## Slide 7: Coronary Sinus Annuloplasty

## Slide 8: Carillon
Coronary Sinus Annuloplasty
Notes: Proximal and distal nitinol self expanding anchors
Steel bridge→manual tension given
Anchor slippage a big problem
CARILLON XE→ modified device→ AMADEUS Trial→ reduction in MR and clinical benefit.

## Slide 9: Percutaneous Transvenous Mitral Annuloplasty Device [PTMA]
Coronary Sinus Annuloplasty
Notes: Metal rods inserted into the coronary sinus→intention to deflect the post portion of mitral annulus anteriorly.

## Slide 10
Percutaneous Transvenous Mitral Annuloplasty Device [PTMA]
Coronary Sinus Annuloplasty
Notes: PTOLEMY trial → 19 patients→ limited durability and reduction in grade of MR

## Slide 11: Monarc
Coronary Sinus Annuloplasty
Notes: Proximal and distal stent like anchors.
Nitinol bridge segement→constructed like a spring with biodegradable spacers→shortens with time→both acute and delayed effect

## Slide 12: Monarc
Coronary Sinus Annuloplasty
Notes: Anatomical considerations
Crossing over LCx and branches→ischemia
More towards atrial side
Coronary sinus lead implantation may cause issues

## Slide 13: Monarc
Coronary Sinus Annuloplasty
Notes: EVOLUTION I → Feasibility trial
EVOLUTION II → Safety and efficacy of MONARC in grade 3&4 functional MR

## Slide 14: Atrial Remodelling Devices

## Slide 15: Percutaneous Septal Shortening System [PS3]
Atrial Remodelling Devices
Notes: Anchors in great cardiac vein and second in IAS fossa ovalis. Magnetic wire delivery system and traction reduces AP diameter of annulus.

## Slide 16: Percutaneous Mitral Repair Device [St. Jude Device]
Atrial Remodelling Devices
Notes: Distal anchors in mitral annulus adjacent to P2 scallop
Proximal anchors in RA near posteromedial trigone
Tether→polyester

## Slide 17: Percutaneous Mitral Repair Device [St. Jude Device]
Atrial Remodelling Devices

## Slide 18: Direct Annuloplasty

## Slide 19: Mitralign
Direct Annuloplasty
Notes: Only 3 anchors in the post annulus. Initially developed as a transapical approach, now transaortic approach available.

## Slide 20: Accucinch
Direct Annuloplasty
Notes: Almost entire mitral annulus is encircled with anchors and tightened

## Slide 21: Accucinch
Direct Annuloplasty

## Slide 22: QuantumCor
Direct Annuloplasty
Notes: High frequency focussed ultrasound → annular collage tissue heating and subsequent shrinkage

## Slide 23: Direct annuloplasty : Hybrid approach
Direct Annuloplasty
Notes: Surgically implanted annuloplasty ring
Percutaneously adjusted via trans-septal approach to tighten

## Slide 24: Ventricular Remodelling devices

## Slide 25: iCoapsys
Ventricular Remodelling Devices
Notes: Coapsys→surgically implanted version of this device
TRACE (feasibility) & RESTORE-MV (RCT) trials
iCoapsys→percutaneous version→inserted via Subxiphoid pericardial access sheath

## Slide 26: Mardil-BACE
Ventricular Remodelling Devices
Notes: Requires mini-thoracotomy. Silicone band placed around mitral annulus with inflatable portions to ↑ tension.
No coronary artery compromise shown in animal models.

## Slide 27: Transcatheter Chordal Implants

## Slide 28: MitraFlex; NeoChord; Babic
Transcatheter Chordal Implants
MitraFlex
NeoChord
Babic
Notes: MitraFlex & NeoChord→ transapical placement of anchors on LV wall and leaflet, connected by an artificial chordae
Babic → transapical insertion of a suture through the leaflet, exteriorized via trans-septal approach from venous side to insert an pledget→apposed to leaflet by pulling guiding sutures from the epicardial end.

## Slide 29: Transcatheter Mitral Valve replacement
TMVR

## Slide 30: Endovalve-Herrmann prosthesis
TMV Replacement
Notes: One of the first devices designed
Now undergoing redesign→permaseal technology to facilitate transapical approach. (sutureless wound closure)

## Slide 31: CardiAQ
TMV Replacement
Notes: Self expanding nitinot frame→ 3 leaflets of bovine pericardial tissue
No radial force on annulus, the anchors clinch the mitral valve from the LA and LV side, foreshortening of the anchor causes a clamping action.
Readjustable before final deployement.
2 percutaneous approaches→transpical and transvenous septal puncture.

## Slide 32: CardiAQ
TMV Replacement

## Slide 33: Tiara valve
TMV Replacement
Notes: Self expanding bioprosthesis with bovine pericardial tissue leaflets
D-shaped→matches annulus
Transapical approach → 32F delivery sheath

## Slide 34: Tendyne valve
TMV Replacement
Notes: Trileaflet pericardial valve with nitinol frame
Transapical approach with neochordae attachement.
D-shaped designs were tried but failed due to reorientation of the valve and ↑ paravalvular leak

## Slide 35: Medtronic-TMV
TMV Replacement
Notes: Trileaflet pericardial valve
Large atrial portion and small ventricular portion to minimize LVOT obstruction.
No radial force, uses MV leaflets for anchorage.
Delivered transatrially. Transseptal delivery under development.

## Slide 36: Fortis TMV
TMV Replacement
Notes: Cloth covered self expanding nitinol frame to minimize PVL.
Enrollment for trial halted due to ↑ valve thrombosis.

## Slide 37: Cardiovalve
TMV Replacement
Notes: Valtech company
Transfemoral route
2 step approach→first sealing polyester skirt, second the actual valve implantation.

## Slide 38: Highlife Medical - TMV
TMV Replacement
Notes: Transfemoral approach
2 step procedure
A&B→placing a locking component in subannular space→transfemoral route
C-F→transatrial route

## Slide 39: Gorman - TMV
TMV Replacement
Notes: Single nitinol wire woven into complex 3D structure, porcine pericardium valve
Requires both radial force and valve gripping anchors

## Slide 40: MitrAssist
TMV Replacement
Notes: Israel
Neither repair nor replacement→works in unison with native mitral valve.
Nitinol frame, pericardial bileaflet tissue valve (asymmetrical design).
Transfemoral transaortic route.
Probably suitable for all types of MR
>90% closure distance promoted by native mitral valves
>80% LV pressure acting on native mitral apparatus

## Slide 41: THANK YOU